## Slide 1
Hands-on AI based 3D Vision
Summer Semester 26
Lecture 5_0 – Surface Reconstruction
Prof. Dr.-Ing Gerard Pons-Moll
University of Tübingen / MPI-Informatics
Notes: Intro

## Slide 2: Increasing complexity of our models
Notes: To model virtual humans (appearance) we need to model at least, the kinematic parameterization and its transformations, which we saw in the previous lecture.
Then we need to model the shape geometry. Finally to obtain a photorealistic result we nee to think about materials, lighting and textures.
The topic of todays lecture is on how to represent geometry.

## Slide 3
Notes: How might you describe
There are many represetations of geometry. Implicit, explicit, by language, as the curve of a dynamical system, discrerte, continuous, by specifying intrinsic shape properties like curvatures etc

## Slide 4
Notes: How might you describe
There are many represetations of geometry. Implicit, explicit, by language, as the curve of a dynamical system, discrerte, continuous, by specifying intrinsic shape properties like curvatures etc

## Slide 5: Examples of geometry

## Slide 6: Examples of geometry

## Slide 7: Examples of geometry
Notes: Think of shape dynamics. The shape might be breaking into smaller pieces and perging again like in a fluid

## Slide 8: Examples of geometry
Notes: We might want to represent a full city, but keep detail. Detail at different scales.
A single mesh might not be the best choice.

## Slide 9: Examples of geometry
Notes: Modelling this with meshes seems like a nightmare. Probably a volumetric representation is beter in this case

## Slide 10: Given all these options, what is the best way to encode geometry on a computer?

## Slide 11: It's a jungle out there!

## Slide 12
Notes: Geometry is hard. Great quote by an expert in geometry, David Baraff, senior research scientist at pxar animation studios:

## Slide 13: Many ways to digitally encode geometry
EXPLICIT
  point cloud
  polygon mesh
  subdivision, NURBS
  …
IMPLICIT
  level set
  algebraic surface
  L-systems
  …
Each choice best suited to a different task/type of geometry
Notes: Lots of representations in computer graphics to represent surfaces

## Slide 14: "Implicit" Representations of Geometry
Points aren't known directly, but satisfy some relationship
E.g., unit sphere is all points such that x2+y2+z2=1
More generally, f(x,y,z) = 0

## Slide 15: Surfaces as an Implicit Function
Notes: This function could be an occupancy indicatory, taking value – if outside and 1 if inside. The surface are the points at the boundary.
f(\mathbf{p}) = \begin{cases}
0, & \mbox{if} \quad \mathbf{p} \in \mathrm{outside} \\
1, & \mbox{if } \quad \mathbf{p} \in \mathrm{inside}
\end{cases}
\mathcal{S} = \{\mathbf{p},\ f(\mathbf{p}) = \tau \}

## Slide 16: Many implicit representations in graphics
Notes: Many implicit representations in graphics. Quite often basic primitives such as ellispoids or Gaussian blobs are used to create complex shapes. In machine learning, implicit function is not closed form, but we use neural network to approximate the implicit function.
We will see some these.

## Slide 20: Algebraic Surfaces (Implicit)
Surface is zero set of a polynomial in x, y, z
Examples:
What about more complicated shapes?
Very hard to come up with polynomials!
Notes: Implicit functions with closed form mathematical expresions. Good because they are easy to evaluate, easy to store. However, hard to create complex shapes.
Hard to come up with polynomials for complex shapes.

## Slide 21: Constructive Solid Geometry (Implicit)
Build more complicated shapes via Boolean operations
Basic operations:
Then chain together expressions:
Notes: Implict allow to make basic operations with shapes, like union, intersection, difference etc

## Slide 22: Blending Distance Functions (Implicit)
A distance function gives distance to closest point on object
Can blend any two distance functions d1, d2:
Similar strategy to points, though many possibilities. E.g.,
Appearance depends on how we combine functions
Q: How do we implement a Boolean union of d1(x), d2(x)?
A: Just take the minimum: f(x) = min(d1(x), d2(x))
Notes: Can blend using distance function

## Slide 23: Scene made of pure signed distance functions Art with math -- really hard!
https://www.shadertoy.com/view/NtlSDs
Notes: Making art with math.

## Slide 24: Nowadays -- Neural Distance Fields (NDF)
INPUT
OUTPUT OF NDF
Chibane et al. NDF, NeurIPS 2020
Notes: While storing an implicit function in a 3D grid is costly. We will see during the lecture neural methods to represent shapes with neural networks.
Essentially the neural network is trained to return for every point in space at which distance from the surface it lies. And from this we can recover the surface

## Slide 25: Distance field, field normals and closest points
Surface normal are the gradients of the function
Closest points are found trivially as:
Distance to surface is given by the distance field itself f(p)
Notes: A good representation should allow to compute closest points and normals easily. With a distance field that is more or less straightforward.
The normal is the gradient of the distance field. Why? Along the levelset the function does not change value. The gradient points towards maximum change.
This needs to be orthogonal to the levelset curve or surface. Hence the gradient is the normal
\mathcal{S} =\{\mathbf{p}\in\mathbb{R}^3 \, | f(\mathbf{p})=0)\}
n(\mathbf{p}) = \nabla f(\mathbf{p})

## Slide 26: Surface Reconstruction from Implicit Representation
Implicit surfaces have some nice features (e.g., merging/splitting)
But, hard to describe complex shapes in closed form
Alternative: store a grid of values approximating function
Surface is found where interpolated values equal zero

## Slide 27: Marching Cubes
Read four slices into memory.
Scan two slices and create a cube from four neighbors on one slice and four neighbors on the next slice.
…
…
…
…
...
Notes: Levelsets widely used for medical imaging. Great for volumes

## Slide 28: Marching Cubes
...
...
Calculate an index for the cube by comparing the eight density values at the cube vertices with the surface constant.
Using the index, look up the list of edges from a precalculated table.
Notes: Levelsets widely used for medical imaging. Great for volumes

## Slide 29: Marching Cubes
...
...
...
...
Using the densities at each edge vertex, find the surface-edge intersection via linear interpolation
Calculate a unit normal at each cube vertex using central differences. Interpolate the normal to each triangle vertex
Output the triangle vertices and vertex normals.
Notes: Levelsets widely used for medical imaging. Great for volumes

## Slide 30: Marching Cubes
Notes: Once we have calculated the values of the implicit function at the vertices of the cube,
we can interpolate the vertices of the mesh representing surface only for the cubes matched against the look up table of the Marching Cubes algorithm

## Slide 31: Challenges with Marching Cubes
Generating one polygon for each portion of the contour
Can only approximate the restriction of the contour
Fails to capture the sharp detail of the surface
Difficult to simplify the generated surface mesh
Becoming challenging to extract surface for higher grid sizes (3D uniform grid induces cubic cost in resolution)
Notes: Problem with matching cubes. Show lack of detail.

## Slide 32: Dual Contouring
Can capture sharp edges along corners of surface
Can leverage gradient information along edge intersections to reproduce a wide class of polyhedral shapes as well as curved or sharp edges
Utilizes octree in place of a 3D uniform grid for better efficiency
Uses normals to define Quadratic Error Function for each leaf of the octree, inspired by original Extended Marching Cubes (EMC)
E[x] = Σi (ni * (x - pi))2
where pi and ni correspond to the intersections and normals of the contour with the edges of cube
Notes: Problem with matching cubes. Show lack of detail.

## Slide 33: Dual Contouring
Signed Grid with edges tagged by Hermite Data
Marching Cubes Contour
Dual Contour
Notes: Hermite Data = (i.e; exact intersection points and normals)

## Slide 34: Challenges with Dual Contouring
Limited expressivity due to reliance on structured grids
Cannot faithfully extract very thin surfaces and features (otherwise requiring very fine grid resolution)
Limited by the amount of surface simplification
Notes: Problem with matching cubes. Show lack of detail.

## Slide 35: Dual Marching Cubes
Align features of the implicit function with the features of the structured grid; enabling extraction of sharp features
Can generate adaptive polygonalizations that are crack-free and topologically manifold
Can reproduce thin features in surface without excessive subdivision of the octree
Notes: Problem with matching cubes. Show lack of detail.

## Slide 36: Dual Marching Cubes
DMC's QEF is calculated by computing a tangent planes to the implicit surface representation f on a grid of points (xi, yi, zi) sampled over c.
Tangent plane's equation: Ti(x, y, z) = ∇f(xi, yi, zi) ((x, y, z) - (xi, yi, zi))
DMC's QEF sums over all sample points yielding:
E(f(x, y, z), x, y, z) = Σi (f(x, y, z) - Ti(x, y, z))2/(1+|∇f(xi, yi, zi)|2)
where the denominator normalizes the contribution of each tangent plane
Notes: Problem with matching cubes. Show lack of detail.

## Slide 37: Comparison between Marching Cubes & Dual Contouring & Dual Marching Cubes
Notes: Comparison between MC, DC and DMC.
MC fails to capture sharp features.
DC captures sharp features but can produce non-manifold vertices in some cases.
DMC do not introduce non-manifold vertices, and can generate crack-free adaptive polygonalization.

## Slide 38: Comparison between Marching Cubes & Dual Contouring & Dual Marching Cubes
Ground Truth Model
Dual Marching Contour
Marching Contour
Dual Contour
Notes: Showing Comparison between Marching Cubes, Dual Contouring and Dual Marching Cubes

## Slide 39: Flexi-Cubes: Flexible Iso-surface Extraction
Notes: PROBLEM with classical methods: non-differentiable. So if I am predicting surfaces or vertices with neural network, I can not supervise directly on surface.
We introduce FlexiCubes, an isosurface representation specifically designed for optimizing an unknown mesh with respect to geometric, visual, or even physical objectives.
Our main insight is to introduce additional carefully-chosen parameters into the representation, which allow local flexible adjustments to the extracted mesh geometry and connectivity.
These parameters are updated along with the underlying scalar field via automatic differentiation when optimizing for a downstream task

## Slide 40: Challenges faced by Level Sets method
Although Level Set representation provides much more explicit control over shape (like a texture), it
runs into problems of aliasing! (Unlike closed-form expressions)
induces O(n3) storage costs for 3D surface extraction
can save space by only storing a narrow band around the surface.
Notes: Efficient storage, use a narrow band.

## Slide 41: Implicit Representations - Pros & Cons
Pros:
description can be very compact (e.g., a polynomial)
easy to determine if a point is in our shape (just plug it in!)
other queries may also be easy (e.g., distance to surface)
for simple shapes, exact description/no sampling error
easy to handle changes in topology (e.g., fluid)
Cons:
expensive to find all points in the shape (e.g., for drawing)
very difficult to model complex shapes

## Slide 42: "Explicit" Representations of Geometry
All points are given directly
E.g., points on sphere are
More generally:
(Might have a bunch of these maps, e.g., one per triangle!)

## Slide 47
Notes: Hard

## Slide 48
Notes: Implicit vs Explicit

## Slide 49: Point Clouds
Easiest representation: list of points (x,y,z)
Often augmented with normals
Easily represent any kind of geometry
Easy to draw dense cloud (>>1 point/pixel)
Hard to interpolate under-sampled regions
Hard to do processing / simulation/...
Notes: Output of many 3D scanners and computer vision reconstruction methods. Hard to render

## Slide 50: From Points to Surfaces
Why do we need surface reconstruction?
Point clouds are discrete, unordered — no connectivity or topology
Downstream tasks (rendering, simulation, 3D printing) require a continuous surface
Goal: a method that is global, robust to noise, and produces watertight meshes
Key idea: recast surface reconstruction as solving a Poisson equation

## Slide 51: Poisson Surface Reconstruction
Kazhdan et al. PSR, ESGP, June 2006
Notes: Reconstructing a surface from a point cloud is an underdetermined problem. Given oriented point cloud, we want to find an indicator function representing a surface such that:
The gradient of the indicator function is a vector field that is zero almost everywhere (since the indicator function is constant almost everywhere),
except at points near the surface, where it is equal to the inward surface normal. Thus, the oriented point samples can be viewed as samples of
the gradient of the model’s indicator function, see Figure.
Absent task-specific knowledge, the predominant geometry processing algorithm for surface reconstruction is Poisson Surface Reconstruction (PSR) [Kazhdan et al. 2006].
PSR encodes volumetric smoothness away from the input point cloud by minimizing the integrated gradient of the surface’s implicit representation and remains one of
the best performing general surface reconstruction algorithms in terms of robustness and efficiency

## Slide 52: Poisson Surface Reconstruction
Given an oriented point cloud P with points 𝑝1, . . . , 𝑝n and corresponding (outward-facing) normal observations 𝑛1, . . . , 𝑛n, we consider the implicit reconstruction task of finding a function 𝑓 : Rd → R such that
𝑓(𝑝𝑖) = 0 , ∇𝑓(𝑝𝑖) = 𝑛𝑖 , ∀𝑖 ∈ {1, . . . , 𝑛} .
PSR first utilizes convolutional kernel F to interpolate 𝑛𝑖 into a vector field V : Rd → Rd defined in box B containing P as
V(x) = Σ𝑖 F(x, x𝑖) 𝑛𝑖
Kazhdan et al. PSR, ESGP, June 2006
Notes: We use a convolutional kernel to approximate the normal.
V is a normal field. F is the Interpolating kernel.

## Slide 53: Poisson Surface Reconstruction
𝑓 : Rd → R is then defined as a function whose gradient best matches V
𝑓 = argmin 𝑔 ∫ 𝐵 ∥V(𝑥) − ∇𝑔(𝑥) ∥2 dx
Variational problem above is equivalent to the Poisson Equation
Δ𝑓 = ∇ V(𝑥)
which is solved by PSR via discretization using the Finite Element Method on an octree and solve using a purpose-built multigrid algorithm
Kazhdan et al. PSR, ESGP, June 2006

## Slide 54: Poisson Surface Reconstruction
𝑓 : Rd → R is then defined as a function whose gradient best matches V
𝑓 = argmin 𝑔 ∫ 𝐵 ∥V(𝑥) − ∇𝑔(𝑥) ∥2 dx
Variational problem above is equivalent to the Poisson Equation
Δ𝑓 = ∇ V(𝑥)
which is solved by PSR via discretization using the Finite Element Method on an octree and solve using a purpose-built multigrid algorithm. In Screened PSR (Kazhdan et.al, 2013) authors use
𝑓 = argmin 𝑔 ∫ B ∥V(𝑥) − ∇𝑔(𝑥) ∥2 dx + α ∗ ∑︁𝑖 g(pi)2
Kazhdan et al. PSR, ESGP, June 2006
Notes: Similar to slide directly before, just a last sentence is different

## Slide 55: (Screened) Poisson reconstruction
Can extract the surface from oriented point clouds
(Screened PSR) efficiently implements sparsity constraints
Can better capture the details of the underlying surface
(Screened PSR) implements efficient octree structure and multigrid algorithm to reduce the time complexity
However, these methods limit themselves to outputting the likeliest surface given the point cloud observations and their assumed prior. Whereas in reality there could be theoretically infinite number of possible surfaces representing same set of Points with normals

## Slide 56: (Screened) Poisson reconstruction
Notes: Figure shows reconstructions results for the Neptune and David models at depth 10. It also shows surface cross-sections overlaid with the validation points in their vicinity.
These images reveal that the Poisson reconstruction (far left), and to a lesser extent the SSD reconstruction (center left), over-smooth the data, while the
Wavelet reconstruction (center left) has apparent derivative discontinuities.
In contrast, screened Poisson approach (far right) provides a reconstruction that faithfully fits the samples without introducing noise.

## Slide 57
Neural Stochastic Screened Poisson Surface Reconstruction
Sellan and Jacobson, Neural Stochastic Screened PSR, SIGGRAPH Asia 2023
Take a step even further and models the posterior multivariate Gaussian distributions representing the likelihood of all possible reconstructions for the given Point Set with normals
Proposes the parametrization of mean and covariance functions using neural networks, optimizing them through gradient-based methods for a more efficient and flexible approach
Enabling computation of the statistical quantities over the reconstruction
Notes: Neural Stochastic Screened PSR parametrize the mean and covariance of the implicit field describing the reconstructed surface using a neural network,
which we optimize using gradient based optimization on losses derived from the variational version of the Poisson equation.
This unique neural formulation also allows us to extend the stochastic perspective beyond the original PSR and into Screened PSR [Kazhdan and Hoppe 2013].

## Slide 58
Neural Stochastic Screened Poisson Surface Reconstruction
Sellan and Jacobson, Neural Stochastic Screened PSR, SIGGRAPH Asia 2023
Notes: Neural Stochastic Screened PSR parametrize the mean and covariance of the implicit field describing the reconstructed surface using a neural network,
which we optimize using gradient based optimization on losses derived from the variational version of the Poisson equation.
This unique neural formulation also allows us to extend the stochastic perspective beyond the original PSR and into Screened PSR [Kazhdan and Hoppe 2013].

## Slide 59
Neural Stochastic Screened Poisson Surface Reconstruction
Sellan and Jacobson, Neural Stochastic Screened PSR, SIGGRAPH Asia 2023
Notes: Theoretically, Neural Stochastic Screened PSR strictly generalizes PSR (see Figure);
in practice, it imposes a volumetric smoothness prior that avoids overfitting.

## Slide 60
Neural Stochastic Screened PSR
Sellan and Jacobson, Neural Stochastic Screened PSR, SIGGRAPH Asia 2023
Notes: Once a point cloud has been captured, Neural Stochastic Screened PSR can be used to compute all kinds of statistical queries useful to the reconstruction
We can use mean and variance predicted by the network to evaluate each point’s cumulative distribution functions at zero, which returns the probability
of any point in space being contained in Ω. Similarly, evaluating the probabilistic density function at zero returns a measure of surface probability

## Slide 61: Polygon Mesh
Store vertices and polygons (most often triangles or quads)
Easier to do processing/simulation, adaptive sampling
More complicated data structures
Irregular neighbourhoods
Notes: Easy to store, lightweight. Easy to process and manipulate a mesh.
Problem: topology!!

## Slide 62: Triangle Mesh (Explicit)
Store vertices as triples of coordinates (x,y,z)
Store triangles as triples of indices (i,j,k)
E.g., tetrahedron:
Use barycentric interpolation to define points inside triangles:

## Slide 63: Triangle Mesh – Normals (Explicit)
Option1: Normals per face (Phong)
Option2: Interpolate incident face normal at each vertex, and interpolate with barycentric interpolation for points inside the triangle
Notes: n = (p_2-p_1)\times{(p_3-p_1)}
n(\phi_1,\phi_2,\phi_3)=\phi_1 n_1 +\phi_2 n_2 + \phi_3 n_3

## Slide 64: Distance queries and closest points
Smooth parametric surface
  Evaluation
  Normals
  Distance and closest point. Find surface point f(u,v) such that:
Mesh
  Distance and closest point:
    Find closest triangle and then find closest point in triangle, and then finding point in triangle
    Use Kd-tree, AAB Tree, to find closest triangles
Notes: [\mathbf{q}-f(u,v)] \times{\mathbf{n}}(u,v)=0
only parallel component

## Slide 65: Subdivision
Alternative starting point for curves/surfaces: subdivision
Start with "control curve"
Repeatedly split, take weighted average to get new positions
For careful choice of averaging rule, approaches nice limit curve
  Often exact same curve as well-known spline schemes!
Notes: Popular alternative are subdivision surfaces.
Start with a control curve. Repeatedly, split the edges, for example in half, and then take a weighted average to get the new vertex positions.
Interesting thing. You get the same curve as some of this curves based on beizer and splits.
Is subdivision implicit or explicit?
Don’t know where the points are. There is no levelset.

## Slide 66: Subdivision Surfaces in Computer Vision
Cashman & Fitzgibbon. What shapes are dolphins?

## Slide 67: Subdivision Surfaces (Explicit)
Start with coarse polygon mesh ("control cage")
Subdivide each element
Update vertices via local averaging
Many possible rules:
  Catmull-Clark (quads)
  Loop (triangles)
  …
Common issues:
  interpolating or approximating?
  continuity at vertices?
Easier than splines for modeling; harder to evaluate pointwise
Widely used in practice (2019 Academy Awards!)
Notes: Common issues: does the limit surface pass through the controlpoints or or just approximates them.
Continuity at vertices?
Easier than splines. No degrees of freedom. Control points control the curve. Harder to evaluate the surface.
Widely used in practice.
More than 4 patches, or fewer than 4 patches meet at a vertex.
Specifically, in 2006, the Academy of Motion Picture Arts and Sciences awarded:
Tony DeRose, Tom Kass, and Tien Truong For their pioneering work in the development of subdivision surfaces used in 3D modeling and animation.

## Slide 68: Subdivision in Pixar (Pixar's "Geri's Game")
Notes: One of the first uses of subdivion surfaces in animation.

## Slide 69: Slide credits and further reading
Keenan Crane – Computer Graphics Lecture CMU 15-462/662. Lecture 09:Introduction to Geometry.

## Slide 70: Aligning Pointclouds to a Common Frame

## Slide 71: Procrustes alignment problem definition
?
Notes: \arg \min_{s,\mathbf{R},\mathbf{t}} \| (s\mathbf{R}\mathbf{V}^T+\mathbf{t})-\mathbf{V}^{\prime T}\|^2_F

## Slide 72: Rigid Alignment
How can we rigidly transform a set of points ?
Translate it
Rotate it
Today we’ll consider also
Scale it
Notes: \mathbf{X}{'} = \mathbf{X} + \mathbf{t}, \mathbf{t} \in \mathbb{R}^3
{\mathbf{X}'}^{T} = \mathbf{R} \cdot \mathbf{X}^T , \mathbf{R} \in \mathbf{SO}(3)
{\mathbf{X}'} = s \mathbf{X} , s \in \mathbb{R}

## Slide 73: Optimisation Problem
Notes: Ideas to solve the problem?
Is it linear, quadratic in the parameters?

## Slide 74: Quick recap of SVD
in general, applied to a real matrix:
warning: this is not the vertex matrix!
Notes: \A &= \U\Sigma \V\tran \\
\A &\equiv (M \times N) \mathrm{\ real\ } \\
\U &\equiv (M\times M) \mathrm{\ orthogonal,\ unit\ norm} \\
\V &\equiv (N\times N) \mathrm{\ orthogonal,\ unit\ norm} \\
\Sigma &\equiv (M\times N) \mathrm{\ diagonal} \\

## Slide 75: Procrustes alignment steps
Optimal rotation obtained by computing SVD on the point cross-covariance
Matrices of points
Translation is the centroid difference
Scale is a quotient of eigenvalue sums
* See also clarification slide 1 at the end of slide deck
Notes: \mathbf{X}= [\mathbf{x}_1 \hdots \mathbf{x}_n]^T
\mathbf{Y}= [\mathbf{y}_1 \hdots \mathbf{y}_n]^T
\mathbf{R} = \mathbf{U}\mathbf{V}^T
\mathbf{t} = \sum \mathbf{R}\bar{\mathbf{x}} - \bar{\mathbf{y}}
\mathbf{t} = \sum \mathbf{R}\bar{\mathbf{x}} - \bar{\mathbf{y}}
\bar{\mathbf{X}}^T\bar{\mathbf{Y}} = \mathbf{U}\Sigma\mathbf{V}^T
\mathbf{s} = \frac{\mathrm{tr}(\Sigma)}{\|\bar{\mathbf{X}}\|_F^2}
clarify what the \bar{X} is

## Slide 76: Proof

## Slide 77: Procrustes derivation: translation
Minimize the L2 distance between
transformed source points and target points

## Slide 78: Procrustes derivation: translation
We remove the elements that do not depend on the translation and solve for t.
Compute the centroid of the point clouds
So given s and R, we can compute the translation t
Notes: The summation is replaced by the centroids. The rotation and scale comes out of the summation.
Take derivative equate to zero and find result
\documentclass[10pt]{article}
\usepackage[usenames]{color} %used for font color
\usepackage{amssymb} %maths
\usepackage{amsmath} %maths
\usepackage[utf8]{inputenc} %useful to type directly diacritic characters
\newcommand*{\tran}{^{\mkern-1.5mu\mathsf{T}}}
\newcommand{\X}{\mathbf{X}}
\newcommand{\mX}{\bar{\mathbf{X}}}
\newcommand{\x}{\mathbf{x}_i}
\newcommand{\mx}{\bar{\mathbf{x}}}
\newcommand{\mxi}{\bar{\mathbf{x}_i}}
\newcommand{\Y}{\mathbf{Y}}
\newcommand{\mY}{\bar{\mathbf{Y}}}
\newcommand{\y}{\mathbf{y}_i}
\newcommand{\my}{\bar{\mathbf{y}}}
\newcommand{\myi}{\bar{\mathbf{y}_i}}
\newcommand{\U}{\mathbf{U}}
\newcommand{\V}{\mathbf{V}}
\newcommand{\R}{\mathbf{R}}
\newcommand{\A}{\mathbf{A}}
\newcommand{\trans}{\mathbf{t}}
\usepackage[normalem]{ulem}
\usepackage{amsmath}
\newcommand{\stkout}[1]{\ifmmode\text{\sout{\ensuremath{#1}}}\else\sout{#1}\fi}
%%%%%%%%%%%%%%%%%%%%%%%%%%%
\X, \Y &\in \mathbb{R}^{(N\times 3)} \\
\x, \y &\in \mathbb{R}^{(3\times 1)} \\
%\mu_\X &= \mathop{}\mathbb{E}(\X), \mu_\Y = \mathop{}\mathbb{E}(\Y) \\
%\bar{\X} &= \X - \mu_\X, \bar{\Y} = \Y - \mu_\Y \\
%\tilde{\X} &= \frac{\bar{\X}}{\|\bar{\X}\|}, \tilde{\Y} = \frac{\bar{\Y}}{\|\bar{\Y}\|} \\
%\A &= \tilde{\X}\tran \tilde{\Y} \\
%\A &= \U \Sigma \V\tran \\
%\R &= \V\U\tran \\
%s &= \mathrm{tr}(\Sigma) \frac{\|\bar{\X}\|}{\|\bar{\Y}\|} \\
%\trans &= \mu\X - s(\mu\Y \cdot \R)
{s, \R, \trans} &= \arg\min_{s, \R, \trans} E \\
E &\equiv \sum_i \| s \R \x + \trans - \y \|^2 \\
&= \sum_i (s \R \x + \trans - \y)\tran (s \R \x + \trans - \y) \\
&= \sum_i s^2 \x\tran \x + \trans\tran \trans + \y\tran \y + 2s\x\tran \R\tran \trans - 2s\x\tran\R\tran \y -2\trans \tran \y \\
{\trans} &= \arg\min_{\trans} E = \arg\min_{\trans}\sum_i \stkout{s^2 \x\tran \x} + \trans\tran \trans + \stkout{\y\tran \y} + 2s\x\tran \R\tran \trans - \stkout{2s\x\tran\R\tran \y} -2\trans \tran \y \\
&= \arg\min_{\trans}\sum_i \trans\tran \trans + 2s\x\tran \R\tran \trans -2\trans \tran \y \\
\mx &\equiv \frac{\sum_i \x}{N}, \my \equiv \frac{\sum_i \y}{N} \\
{\trans} &= \arg\min_{\trans} E = \arg\min_{\trans}(\trans\tran (2s\R \mx + \trans - 2\my)) = \my - s \R \mx \\
\mxi &\equiv \x - \mx, \myi \equiv \y - \my \\
E &= \sum_i \| s \R \x + \trans - \y \|^2 = \sum_i \| s \R \mxi - \myi \|^2 = \sum_i s^2 \mxi\tran \mxi + \myi\tran \myi - 2s\mxi\tran\R\tran \myi \\
\A &\equiv \mX\tran \mY = \sum_i \mx\my\tran\\
{\R} &= \arg\min_{\R} E = \arg\min_{\R}(\sum_i \stkout{s^2 \mxi\tran \mxi + \myi\tran \myi} - 2s\mxi\tran\R\tran \myi)\\
&= \arg\max_{\R}(\sum_i \mxi\tran\R\tran \myi) = \arg\max_{\R}(\sum_i \mathrm{tr}(\mxi\myi\tran \R)) = \mathrm{tr}(\A \R) \\
\A &= \U\Sigma\V\tran \mathrm{,\ through\ SVD}\\
\R &= \V\U\tran \mathrm{\ because\ } \\
\A\R &= (\U\Sigma\V\tran)(\V\U\tran) = \U\Sigma\U\tran \mathrm{\ symmetric\ positive\ semidefinite,\ so\ } \R \mathrm{\ maximizes\ } \mathrm{tr}(\A\R) \\
s &= \arg\min_{s} E = \arg\min_{s}(\sum_i s^2 \mxi\tran \mxi + \stkout{\myi\tran \myi} - 2s\mxi\tran\R\tran \myi) \\
&= \arg\min_{s}(s^2 \sum_i(\mxi\tran \mxi) -2s \sum_i(\mxi\tran\R\tran \myi)) \\
&= \arg\min_s(s^2a -2sb) = \frac{b}{a} = \frac{\mxi\tran\R\tran \myi}{\mxi\tran \mxi} \\
&= \frac{\mathrm{tr}(\A\R)}{\|\X\|^2} = \frac{\mathrm{tr}(\Sigma)}{\|\X\|^2}

## Slide 79: Procrustes derivation: Rotation
Subtract the centroid from the points to obtain a simpler expression for E
Optimal rotation does not depend on scale
Notes: Let’s look at the rotation part
\mathbf{R} &= \arg\min_\mathbf{R} ||\mathbf{R} \bar{\mathbf{X}}^T-\bar{\mathbf{Y}}^T\|_F^2 \\
&= \arg\min_\mathbf{R} \langle \mathbf{R} \bar{\mathbf{X}}^T-\bar{\mathbf{Y}}^T, \mathbf{R} \bar{\mathbf{X}}^T-\bar{\mathbf{Y}}^T \rangle_F \\
&= \arg\min_\mathbf{R} \|\mathbf{R} \bar{\mathbf{X}}^T\|_F^2 + \|\bar{\mathbf{Y}}^T\|_F^2 - 2 \langle \mathbf{R} \bar{\mathbf{X}}^T , \bar{\mathbf{Y}}^T \rangle_F \\
&= \arg\min_\mathbf{R} \|\bar{\mathbf{X}}^T\|_F^2 + \|\bar{\mathbf{Y}}^T\|_F^2 - 2 \langle \mathbf{R} \bar{\mathbf{X}}^T , \bar{\mathbf{Y}}^T \rangle_F \\
&= \arg\max_\mathbf{R} \langle \mathbf{R} , \bar{\mathbf{Y}}^T \bar{\mathbf{X}} \rangle_F \\
&= \arg\max_\mathbf{R} \langle \mathbf{R}, U\Sigma V^T \rangle_F \\
&= \arg\max_\mathbf{R} \langle U^T \mathbf{R} V , \Sigma \rangle_F \\
&= \arg\max_\mathbf{R} \langle S , \Sigma \rangle_F \quad \text{where } S = U^T \mathbf{R} V \\

## Slide 80: Procrustes derivation: Rotation
Inner product should be maximum!
Rotation does not change norm!
Subtract the centroid from the points to obtain a simpler expression for E
Optimal rotation does not depend on scale

## Slide 81: Procrustes derivation: Rotation
Optimal rotation does not depend on scale
Inner product should be maximum!
Rotation does not change norm!
Cross-covariance matrix
SVD decomposition
Subtract the centroid from the points to obtain a simpler expression for E
Notes: \mathbf{R} &= \arg\min_\mathbf{R} ||\mathbf{R} \bar{\mathbf{X}}^T-\bar{\mathbf{Y}}^T\|_F^2 \\
&= \arg\min_\mathbf{R} \langle \mathbf{R} \bar{\mathbf{X}}^T-\bar{\mathbf{Y}}^T, \mathbf{R} \bar{\mathbf{X}}^T-\bar{\mathbf{Y}}^T \rangle_F \\
&= \arg\min_\mathbf{R} \|\mathbf{R} \bar{\mathbf{X}}^T\|_F^2 + \|\bar{\mathbf{Y}}^T\|_F^2 - 2 \langle \mathbf{R} \bar{\mathbf{X}}^T , \bar{\mathbf{Y}}^T \rangle_F \\
&= \arg\min_\mathbf{R} \|\bar{\mathbf{X}}^T\|_F^2 + \|\bar{\mathbf{Y}}^T\|_F^2 - 2 \langle \mathbf{R} \bar{\mathbf{X}}^T , \bar{\mathbf{Y}}^T \rangle_F \\
&= \arg\max_\mathbf{R} \langle \mathbf{R} , \bar{\mathbf{Y}}^T \bar{\mathbf{X}} \rangle_F \\
&= \arg\max_\mathbf{R} \langle \mathbf{R}, U\Sigma V^T \rangle_F \\
&= \arg\max_\mathbf{R} \langle U^T \mathbf{R} V , \Sigma \rangle_F \\
&= \arg\max_\mathbf{R} \langle S , \Sigma \rangle_F \quad \text{where } S = U^T \mathbf{R} V \\

## Slide 82: Procrustes derivation: Rotation
What kind of matrix is ?
What kind of matrix is ?
Orthogonal
Diagonal
Notes: \mathbf{R} &= \arg\min_\mathbf{R} ||\mathbf{R} \bar{\mathbf{X}}-\bar{\mathbf{Y}}\|_F^2 \\
&= \arg\min_\mathbf{R} \langle \mathbf{R} \bar{\mathbf{X}}-\bar{\mathbf{Y}}, \mathbf{R} \bar{\mathbf{X}}-\bar{\mathbf{Y}} \rangle_F \\
&= \arg\min_\mathbf{R} \|\mathbf{R} \bar{\mathbf{X}}\|_F^2 + \|\bar{\mathbf{Y}}\|_F^2 - 2 \langle \mathbf{R} \bar{\mathbf{X}} , \bar{\mathbf{Y}} \rangle_F \\
&= \arg\min_\mathbf{R} \|\bar{\mathbf{X}}\|_F^2 + \|\bar{\mathbf{Y}}\|_F^2 - 2 \langle \mathbf{R} \bar{\mathbf{X}} , \bar{\mathbf{Y}} \rangle_F \\
&= \arg\max_\mathbf{R} \langle \mathbf{R} , \bar{\mathbf{Y}} \bar{\mathbf{X}}^T \rangle_F \\
&= \arg\max_\mathbf{R} \langle \mathbf{R}, U\Sigma V^T \rangle_F \\
&= \arg\max_\mathbf{R} \langle U^T \mathbf{R} V , \Sigma \rangle_F \\
&= \arg\max_\mathbf{R} \langle S , \Sigma \rangle_F \quad \text{where } S = U^T \mathbf{R} V \\

## Slide 83: Procrustes derivation: Rotation
What kind of matrix is ?
What kind of matrix is ?
Orthogonal
Diagonal
Hence the quantity above is maximised when equals the identity, hence:
SVD of cross-covariance of pointsclouds
Notes: \mathbf{R} &= \arg\min_\mathbf{R} ||\mathbf{R} \bar{\mathbf{X}}-\bar{\mathbf{Y}}\|_F^2 \\
&= \arg\min_\mathbf{R} \langle \mathbf{R} \bar{\mathbf{X}}-\bar{\mathbf{Y}}, \mathbf{R} \bar{\mathbf{X}}-\bar{\mathbf{Y}} \rangle_F \\
&= \arg\min_\mathbf{R} \|\mathbf{R} \bar{\mathbf{X}}\|_F^2 + \|\bar{\mathbf{Y}}\|_F^2 - 2 \langle \mathbf{R} \bar{\mathbf{X}} , \bar{\mathbf{Y}} \rangle_F \\
&= \arg\min_\mathbf{R} \|\bar{\mathbf{X}}\|_F^2 + \|\bar{\mathbf{Y}}\|_F^2 - 2 \langle \mathbf{R} \bar{\mathbf{X}} , \bar{\mathbf{Y}} \rangle_F \\
&= \arg\max_\mathbf{R} \langle \mathbf{R} , \bar{\mathbf{Y}} \bar{\mathbf{X}}^T \rangle_F \\
&= \arg\max_\mathbf{R} \langle \mathbf{R}, U\Sigma V^T \rangle_F \\
&= \arg\max_\mathbf{R} \langle U^T \mathbf{R} V , \Sigma \rangle_F \\
&= \arg\max_\mathbf{R} \langle S , \Sigma \rangle_F \quad \text{where } S = U^T \mathbf{R} V \\
\bar{\mathbf {Y}}^T\mathbf{X} = \mathbf{{U}}\Sigma\mathbf{{V}}^T

## Slide 84: Procrustes derivation: scale
Optimize scale given the rotation
We used:
Trace invariance with shifts
Trace equals sum of eigenvals for square matrices
Notes: Correction: summation missing
Theorem 1: The trace of a square matrix is smaller than the sum of its eigenvalues, equal if an only if the matrix is symmetric and positive semi-definite
Theorem 2: For a square matrix $\mathbf{B}$, there is an orthogonal matrix $\mathbf{C}$ such that $\mathbf{B}\mathbf{C}$ is symmetric and positive semi-definite. If $\mathbf{D}$ is any other orthogonal matrix, $\mathrm{tr}(\m
athbf{B}\mathbf{D}) \leq \mathrm{tr}(\mathbf{B}\mathbf{C})$, equal if and only if $\mathbf{B}\mathbf{D}$ is symmetric and positive semi-definite
change A by Sigma
\mathrm{tr}\{ \mathbf{X} \mathbf{R}^T \mathbf{Y} \}
=\frac{\mathrm{tr}(\bar{\mathbf{X}} \mathbf{R}^T \bar{\mathbf{Y}}^T)}{\|\bar{\mathbf{X}}\|_F^2} = \frac{\mathrm{tr}(\mathbf{R}^T\bar{\mathbf{Y}}^T\bar{\mathbf{X}})}{\| \bar{\mathbf{X}}\|_F^2}=\frac{\mathrm{tr}(\mathbf{V}\mathbf{U}^T\mathbf{U}\Sigma\mathbf{
V}^T)}{\| \bar{\mathbf{X}}\|_F^2}=\frac{\mathrm{tr}(\Sigma)}{\| \bar{\mathbf{X}}\|_F^2}
\bar{\mathbf{Y}}^T\bar{\mathbf{X}} = \mathbf{U} \Sigma \mathbf{V}^T, \, \mathbf{R} = \mathbf{U}\mathbf{V}^T

## Slide 85: Slide credits and further reading

## Slide 86: Hands-On AI Based 3D Vision Summer Semester 26
Lecture 5_2 – Procrustes Alignment
Prof. Dr.-Ing. Gerard Pons-Moll
University of Tübingen / MPI-Informatics

## Slide 87: Goal: learn a model of pose and shape

## Slide 88: Scan a Lot of People
Notes: The key idea is to scan lots of people

## Slide 89: In lots of poses
Notes: Idea scan lots of people

## Slide 90: To learn a model we need correspondence
Notes: And bring them into correspondence

## Slide 91: Non-rigid Articulated Registration
How?
Notes: We need non-rigid articulated registration

## Slide 92: Today: Rigid Alignment (Procrustes)
?
Notes: Topic of today. Rigid alignment.
\underset{S}{\text{arg min}} || (s\mathbf{R} \cdot \mathbf{X}^T + \mathbf{t}) - \mathbf{X}^{'T}||

## Slide 93: Surface representation: Mesh
Notes: and their corresponding N vertices V define a triangulated mesh, which is a piecewise-linear 2D surface embedded in 3D. We denote those 2D spaces embedded in 3D with calligraphic notation

## Slide 94: Surface representation: Mesh
Notes: A set of M triangles F
\mathcal{V} &\equiv \left\{
\begin{array}{rl}
\mathbf{F} \in \mathbb{N}^{M\times3} \\
\mathbf{V} \in \mathbb{R}^{N\times3}
\end{array} \right. \\
\mathcal{V} &\equiv \mathbb{R}^2 \rightarrow \mathbb{R}^3

## Slide 95: Surface representation: Mesh
How can we rigidly transform a set of points ?
Translate it
Rotate it
Today we’ll consider also
Scale it
Notes: \mathbf{X}{'} = \mathbf{X} + \mathbf{t}, \mathbf{t} \in \mathbb{R}^3
{\mathbf{X}'}^{T} = \mathbf{R} \cdot \mathbf{X}^T , \mathbf{R} \in \mathbf{SO}(3)
{\mathbf{X}'} = s \mathbf{X} , s \in \mathbb{R}

## Slide 96: Rigid transformation + scale
Notes: Algebraically, rotations can be represented by a 3x3 matrix. A column vector v gets pre-multiplied by the rotation matrix R to obtain the rotated point v’ as a column vector. This representation of rotations requires 9 numbers, although there are only 3 degrees of freedom.

## Slide 97: Rigid transformation + scale
Notes: Algebraically, rotations can be represented by a 3x3 matrix. A column vector v gets pre-multiplied by the rotation matrix R to obtain the rotated point v’ as a column vector. This representation of rotations requires 9 numbers, although there are only 3 degrees of freedom.
{\color[rgb]{0.568627,0.384314,0.062745} R }&: \mathbb{R}^3 \rightarrow \mathbb{R}^3\\
\mathbf{v}' &= {\color[rgb]{0.568627,0.384314,0.062745} R }{\color[rgb]{0.643137,0.686275,0.749020} \mathbf{v}} \\
{\color[rgb]{0.568627,0.384314,0.062745} R }& \equiv \left[ \mathbf{r}_x~\mathbf{r}_y~\mathbf{r}_z\right]

## Slide 98: Rigid transformation + scale
Notes: Algebraically, rotations can be represented by a 3x3 matrix. A column vector v gets pre-multiplied by the rotation matrix R to obtain the rotated point v’ as a column vector. This representation of rotations requires 9 numbers, although there are only 3 degrees of freedom.
{\color[rgb]{0.568627,0.384314,0.062745} R }&: \mathbb{R}^3 \rightarrow \mathbb{R}^3\\
\mathbf{v}' &= {\color[rgb]{0.568627,0.384314,0.062745} R }{\color[rgb]{0.643137,0.686275,0.749020} \mathbf{v}} \\
{\color[rgb]{0.568627,0.384314,0.062745} R }& \equiv \left[ \mathbf{r}_x~\mathbf{r}_y~\mathbf{r}_z\right]

## Slide 99: Rigid transformation + scale
Notes: Algebraically, rotations can be represented by a 3x3 matrix. A column vector v gets pre-multiplied by the rotation matrix R to obtain the rotated point v’ as a column vector. This representation of rotations requires 9 numbers, although there are only 3 degrees of freedom.
{\color[rgb]{0.568627,0.384314,0.062745} R }&: \mathbb{R}^3 \rightarrow \mathbb{R}^3\\
\mathbf{v}' &= {\color[rgb]{0.568627,0.384314,0.062745} R }{\color[rgb]{0.643137,0.686275,0.749020} \mathbf{v}} \\
{\color[rgb]{0.568627,0.384314,0.062745} R }& \equiv \left[ \mathbf{r}_x~\mathbf{r}_y~\mathbf{r}_z\right]

## Slide 100: Procrustes alignment problem definition
?

## Slide 101: Procrustes alignment problem definition
Notes: \mathbf{X}' = S(\mathbf{X}) = (s\mathbf{R} \cdot \mathbf{X}^T + \mathbf{t})^T

## Slide 102: Procrustes alignment problem definition
?
Notes: \arg \min_{s,\mathbf{R},\mathbf{t}} \| (s\mathbf{R}\mathbf{V}^T+\mathbf{t})-\mathbf{V}^{\prime T}\|^2_F

## Slide 103: Why Procrustes?
The name Procrustes (Greek: Προκρούστης) refers to a bandit from Greek mythology who made his victims fit his bed either by stretching their limbs or cutting them off.
Prcrustes means “he who stretches”
Notes: Procrustes, which means "he who stretches", offered hospitality to people who passed his home. He gave them a room and a nice bed to sleep in, and he explained to his guests that the bed had a unique quality, in which it would fit whoever laid on it perfectly. He neglected to explain, though, that the reason people fit the bed was due to the fact that he stretched out people who were too short for the bed, and he cut off limbs of people who were too tall for it.
Eventually, a hero in Greek mythology, Theseus, beat Procrustes by adjusting him to fit his own bed.

## Slide 104: Optimisation Problem
Notes: Ideas to solve the problem?
Is it linear, quadratic in the parameters?

## Slide 105: Quick recap of SVD
T
Notes: To understand how procrustes works, we need to understand what SVD does. I assume you are familiar with SVD, but here is a quick recap.
SVD states that every matrix, can be factorized into 3 matrices. Where V and U are orthogonal matrices and sigma is diagonal.
Geometrically it is telling us, a linear mapping can always be decomposed into a rotation, a scaling along principal axis by Sigma, followed by another rotation.

## Slide 106: Quick recap of SVD
in general, applied to a real matrix:
warning: this is not the vertex matrix!
Notes: \A &= \U\Sigma \V\tran \\
\A &\equiv (M \times N) \mathrm{\ real\ } \\
\U &\equiv (M\times M) \mathrm{\ orthogonal,\ unit\ norm} \\
\V &\equiv (N\times N) \mathrm{\ orthogonal,\ unit\ norm} \\
\Sigma &\equiv (M\times N) \mathrm{\ diagonal} \\

## Slide 107: Procrustes alignment steps
Optimal rotation obtained by computing SVD on the point cross-covariance
Matrices of points
Translation is the centroid difference
Scale is a quotient of eigenvalue sums
* See also clarification slide 1 at the end of slide deck
Notes: \mathbf{X}= [\mathbf{x}_1 \hdots \mathbf{x}_n]^T
\mathbf{Y}= [\mathbf{y}_1 \hdots \mathbf{y}_n]^T
\mathbf{R} = \mathbf{U}\mathbf{V}^T
\mathbf{t} = \sum \mathbf{R}\bar{\mathbf{x}} - \bar{\mathbf{y}}
\mathbf{t} = \sum \mathbf{R}\bar{\mathbf{x}} - \bar{\mathbf{y}}
\bar{\mathbf{X}}^T\bar{\mathbf{Y}} = \mathbf{U}\Sigma\mathbf{V}^T
\mathbf{s} = \frac{\mathrm{tr}(\Sigma)}{\|\bar{\mathbf{X}}\|_F^2}
clarify what the \bar{X} is

## Slide 108: Proof

## Slide 109: Procrustes derivation: translation
Minimize the L2 distance between
transformed source points and target points

## Slide 110: Procrustes derivation: translation
We remove the elements that do not depend on the translation and solve for t.
Compute the centroid of the point clouds
So given s and R, we can compute the translation t
Notes: The summation is replaced by the centroids. The rotation and scale comes out of the summation.
Take derivative equate to zero and find result
\documentclass[10pt]{article}
\usepackage[usenames]{color} %used for font color
\usepackage{amssymb} %maths
\usepackage{amsmath} %maths
\usepackage[utf8]{inputenc} %useful to type directly diacritic characters
\newcommand*{\tran}{^{\mkern-1.5mu\mathsf{T}}}
\newcommand{\X}{\mathbf{X}}
\newcommand{\mX}{\bar{\mathbf{X}}}
\newcommand{\x}{\mathbf{x}_i}
\newcommand{\mx}{\bar{\mathbf{x}}}
\newcommand{\mxi}{\bar{\mathbf{x}_i}}
\newcommand{\Y}{\mathbf{Y}}
\newcommand{\mY}{\bar{\mathbf{Y}}}
\newcommand{\y}{\mathbf{y}_i}
\newcommand{\my}{\bar{\mathbf{y}}}
\newcommand{\myi}{\bar{\mathbf{y}_i}}
\newcommand{\U}{\mathbf{U}}
\newcommand{\V}{\mathbf{V}}
\newcommand{\R}{\mathbf{R}}
\newcommand{\A}{\mathbf{A}}
\newcommand{\trans}{\mathbf{t}}
\usepackage[normalem]{ulem}
\usepackage{amsmath}
\newcommand{\stkout}[1]{\ifmmode\text{\sout{\ensuremath{#1}}}\else\sout{#1}\fi}
%%%%%%%%%%%%%%%%%%%%%%%%%%%
\X, \Y &\in \mathbb{R}^{(N\times 3)} \\
\x, \y &\in \mathbb{R}^{(3\times 1)} \\
%\mu_\X &= \mathop{}\mathbb{E}(\X), \mu_\Y = \mathop{}\mathbb{E}(\Y) \\
%\bar{\X} &= \X - \mu_\X, \bar{\Y} = \Y - \mu_\Y \\
%\tilde{\X} &= \frac{\bar{\X}}{\|\bar{\X}\|}, \tilde{\Y} = \frac{\bar{\Y}}{\|\bar{\Y}\|} \\
%\A &= \tilde{\X}\tran \tilde{\Y} \\
%\A &= \U \Sigma \V\tran \\
%\R &= \V\U\tran \\
%s &= \mathrm{tr}(\Sigma) \frac{\|\bar{\X}\|}{\|\bar{\Y}\|} \\
%\trans &= \mu\X - s(\mu\Y \cdot \R)
{s, \R, \trans} &= \arg\min_{s, \R, \trans} E \\
E &\equiv \sum_i \| s \R \x + \trans - \y \|^2 \\
&= \sum_i (s \R \x + \trans - \y)\tran (s \R \x + \trans - \y) \\
&= \sum_i s^2 \x\tran \x + \trans\tran \trans + \y\tran \y + 2s\x\tran \R\tran \trans - 2s\x\tran\R\tran \y -2\trans \tran \y \\
{\trans} &= \arg\min_{\trans} E = \arg\min_{\trans}\sum_i \stkout{s^2 \x\tran \x} + \trans\tran \trans + \stkout{\y\tran \y} + 2s\x\tran \R\tran \trans - \stkout{2s\x\tran\R\tran \y} -2\trans \tran \y \\
&= \arg\min_{\trans}\sum_i \trans\tran \trans + 2s\x\tran \R\tran \trans -2\trans \tran \y \\
\mx &\equiv \frac{\sum_i \x}{N}, \my \equiv \frac{\sum_i \y}{N} \\
{\trans} &= \arg\min_{\trans} E = \arg\min_{\trans}(\trans\tran (2s\R \mx + \trans - 2\my)) = \my - s \R \mx \\
\mxi &\equiv \x - \mx, \myi \equiv \y - \my \\
E &= \sum_i \| s \R \x + \trans - \y \|^2 = \sum_i \| s \R \mxi - \myi \|^2 = \sum_i s^2 \mxi\tran \mxi + \myi\tran \myi - 2s\mxi\tran\R\tran \myi \\
\A &\equiv \mX\tran \mY = \sum_i \mx\my\tran\\
{\R} &= \arg\min_{\R} E = \arg\min_{\R}(\sum_i \stkout{s^2 \mxi\tran \mxi + \myi\tran \myi} - 2s\mxi\tran\R\tran \myi)\\
&= \arg\max_{\R}(\sum_i \mxi\tran\R\tran \myi) = \arg\max_{\R}(\sum_i \mathrm{tr}(\mxi\myi\tran \R)) = \mathrm{tr}(\A \R) \\
\A &= \U\Sigma\V\tran \mathrm{,\ through\ SVD}\\
\R &= \V\U\tran \mathrm{\ because\ } \\
\A\R &= (\U\Sigma\V\tran)(\V\U\tran) = \U\Sigma\U\tran \mathrm{\ symmetric\ positive\ semidefinite,\ so\ } \R \mathrm{\ maximizes\ } \mathrm{tr}(\A\R) \\
s &= \arg\min_{s} E = \arg\min_{s}(\sum_i s^2 \mxi\tran \mxi + \stkout{\myi\tran \myi} - 2s\mxi\tran\R\tran \myi) \\
&= \arg\min_{s}(s^2 \sum_i(\mxi\tran \mxi) -2s \sum_i(\mxi\tran\R\tran \myi)) \\
&= \arg\min_s(s^2a -2sb) = \frac{b}{a} = \frac{\mxi\tran\R\tran \myi}{\mxi\tran \mxi} \\
&= \frac{\mathrm{tr}(\A\R)}{\|\X\|^2} = \frac{\mathrm{tr}(\Sigma)}{\|\X\|^2}

## Slide 111: Procrustes derivation: Rotation
Subtract the centroid from the points to obtain a simpler expression for E
Optimal rotation does not depend on scale
Notes: Let’s look at the rotation part
\mathbf{R} &= \arg\min_\mathbf{R} ||\mathbf{R} \bar{\mathbf{X}}^T-\bar{\mathbf{Y}}^T\|_F^2 \\
&= \arg\min_\mathbf{R} \langle \mathbf{R} \bar{\mathbf{X}}^T-\bar{\mathbf{Y}}^T, \mathbf{R} \bar{\mathbf{X}}^T-\bar{\mathbf{Y}}^T \rangle_F \\
&= \arg\min_\mathbf{R} \|\mathbf{R} \bar{\mathbf{X}}^T\|_F^2 + \|\bar{\mathbf{Y}}^T\|_F^2 - 2 \langle \mathbf{R} \bar{\mathbf{X}}^T , \bar{\mathbf{Y}}^T \rangle_F \\
&= \arg\min_\mathbf{R} \|\bar{\mathbf{X}}^T\|_F^2 + \|\bar{\mathbf{Y}}^T\|_F^2 - 2 \langle \mathbf{R} \bar{\mathbf{X}}^T , \bar{\mathbf{Y}}^T \rangle_F \\
&= \arg\max_\mathbf{R} \langle \mathbf{R} , \bar{\mathbf{Y}}^T \bar{\mathbf{X}} \rangle_F \\
&= \arg\max_\mathbf{R} \langle \mathbf{R}, U\Sigma V^T \rangle_F \\
&= \arg\max_\mathbf{R} \langle U^T \mathbf{R} V , \Sigma \rangle_F \\
&= \arg\max_\mathbf{R} \langle S , \Sigma \rangle_F \quad \text{where } S = U^T \mathbf{R} V \\

## Slide 112: Procrustes derivation: Rotation
Inner product should be maximum!
Rotation does not change norm!
Subtract the centroid from the points to obtain a simpler expression for E
Optimal rotation does not depend on scale

## Slide 113: Procrustes derivation: Rotation
Optimal rotation does not depend on scale
Inner product should be maximum!
Rotation does not change norm!
Cross-covariance matrix
SVD decomposition
Subtract the centroid from the points to obtain a simpler expression for E
Notes: \mathbf{R} &= \arg\min_\mathbf{R} ||\mathbf{R} \bar{\mathbf{X}}^T-\bar{\mathbf{Y}}^T\|_F^2 \\
&= \arg\min_\mathbf{R} \langle \mathbf{R} \bar{\mathbf{X}}^T-\bar{\mathbf{Y}}^T, \mathbf{R} \bar{\mathbf{X}}^T-\bar{\mathbf{Y}}^T \rangle_F \\
&= \arg\min_\mathbf{R} \|\mathbf{R} \bar{\mathbf{X}}^T\|_F^2 + \|\bar{\mathbf{Y}}^T\|_F^2 - 2 \langle \mathbf{R} \bar{\mathbf{X}}^T , \bar{\mathbf{Y}}^T \rangle_F \\
&= \arg\min_\mathbf{R} \|\bar{\mathbf{X}}^T\|_F^2 + \|\bar{\mathbf{Y}}^T\|_F^2 - 2 \langle \mathbf{R} \bar{\mathbf{X}}^T , \bar{\mathbf{Y}}^T \rangle_F \\
&= \arg\max_\mathbf{R} \langle \mathbf{R} , \bar{\mathbf{Y}}^T \bar{\mathbf{X}} \rangle_F \\
&= \arg\max_\mathbf{R} \langle \mathbf{R}, U\Sigma V^T \rangle_F \\
&= \arg\max_\mathbf{R} \langle U^T \mathbf{R} V , \Sigma \rangle_F \\
&= \arg\max_\mathbf{R} \langle S , \Sigma \rangle_F \quad \text{where } S = U^T \mathbf{R} V \\

## Slide 114: Procrustes derivation: Rotation
What kind of matrix is ?
What kind of matrix is ?
Orthogonal
Diagonal
Notes: \mathbf{R} &= \arg\min_\mathbf{R} ||\mathbf{R} \bar{\mathbf{X}}-\bar{\mathbf{Y}}\|_F^2 \\
&= \arg\min_\mathbf{R} \langle \mathbf{R} \bar{\mathbf{X}}-\bar{\mathbf{Y}}, \mathbf{R} \bar{\mathbf{X}}-\bar{\mathbf{Y}} \rangle_F \\
&= \arg\min_\mathbf{R} \|\mathbf{R} \bar{\mathbf{X}}\|_F^2 + \|\bar{\mathbf{Y}}\|_F^2 - 2 \langle \mathbf{R} \bar{\mathbf{X}} , \bar{\mathbf{Y}} \rangle_F \\
&= \arg\min_\mathbf{R} \|\bar{\mathbf{X}}\|_F^2 + \|\bar{\mathbf{Y}}\|_F^2 - 2 \langle \mathbf{R} \bar{\mathbf{X}} , \bar{\mathbf{Y}} \rangle_F \\
&= \arg\max_\mathbf{R} \langle \mathbf{R} , \bar{\mathbf{Y}} \bar{\mathbf{X}}^T \rangle_F \\
&= \arg\max_\mathbf{R} \langle \mathbf{R}, U\Sigma V^T \rangle_F \\
&= \arg\max_\mathbf{R} \langle U^T \mathbf{R} V , \Sigma \rangle_F \\
&= \arg\max_\mathbf{R} \langle S , \Sigma \rangle_F \quad \text{where } S = U^T \mathbf{R} V \\

## Slide 115: Procrustes derivation: Rotation
What kind of matrix is ?
What kind of matrix is ?
Orthogonal
Diagonal
Hence the quantity above is maximised when equals the identity, hence:
SVD of cross-covariance of pointsclouds
Notes: \mathbf{R} &= \arg\min_\mathbf{R} ||\mathbf{R} \bar{\mathbf{X}}-\bar{\mathbf{Y}}\|_F^2 \\
&= \arg\min_\mathbf{R} \langle \mathbf{R} \bar{\mathbf{X}}-\bar{\mathbf{Y}}, \mathbf{R} \bar{\mathbf{X}}-\bar{\mathbf{Y}} \rangle_F \\
&= \arg\min_\mathbf{R} \|\mathbf{R} \bar{\mathbf{X}}\|_F^2 + \|\bar{\mathbf{Y}}\|_F^2 - 2 \langle \mathbf{R} \bar{\mathbf{X}} , \bar{\mathbf{Y}} \rangle_F \\
&= \arg\min_\mathbf{R} \|\bar{\mathbf{X}}\|_F^2 + \|\bar{\mathbf{Y}}\|_F^2 - 2 \langle \mathbf{R} \bar{\mathbf{X}} , \bar{\mathbf{Y}} \rangle_F \\
&= \arg\max_\mathbf{R} \langle \mathbf{R} , \bar{\mathbf{Y}} \bar{\mathbf{X}}^T \rangle_F \\
&= \arg\max_\mathbf{R} \langle \mathbf{R}, U\Sigma V^T \rangle_F \\
&= \arg\max_\mathbf{R} \langle U^T \mathbf{R} V , \Sigma \rangle_F \\
&= \arg\max_\mathbf{R} \langle S , \Sigma \rangle_F \quad \text{where } S = U^T \mathbf{R} V \\
\bar{\mathbf {Y}}^T\mathbf{X} = \mathbf{{U}}\Sigma\mathbf{{V}}^T

## Slide 116: Procrustes derivation: scale
Optimize scale given the rotation
We used:
Trace invariance with shifts
Trace equals sum of eigenvals for square matrices
Notes: Correction: summation missing
Theorem 1: The trace of a square matrix is smaller than the sum of its eigenvalues, equal if an only if the matrix is symmetric and positive semi-definite
Theorem 2: For a square matrix $\mathbf{B}$, there is an orthogonal matrix $\mathbf{C}$ such that $\mathbf{B}\mathbf{C}$ is symmetric and positive semi-definite. If $\mathbf{D}$ is any other orthogonal matrix, $\mathrm{tr}(\m
athbf{B}\mathbf{D}) \leq \mathrm{tr}(\mathbf{B}\mathbf{C})$, equal if and only if $\mathbf{B}\mathbf{D}$ is symmetric and positive semi-definite
change A by Sigma
\mathrm{tr}\{ \mathbf{X} \mathbf{R}^T \mathbf{Y} \}
=\frac{\mathrm{tr}(\bar{\mathbf{X}} \mathbf{R}^T \bar{\mathbf{Y}}^T)}{\|\bar{\mathbf{X}}\|_F^2} = \frac{\mathrm{tr}(\mathbf{R}^T\bar{\mathbf{Y}}^T\bar{\mathbf{X}})}{\| \bar{\mathbf{X}}\|_F^2}=\frac{\mathrm{tr}(\mathbf{V}\mathbf{U}^T\mathbf{U}\Sigma\mathbf{
V}^T)}{\| \bar{\mathbf{X}}\|_F^2}=\frac{\mathrm{tr}(\Sigma)}{\| \bar{\mathbf{X}}\|_F^2}
\bar{\mathbf{Y}}^T\bar{\mathbf{X}} = \mathbf{U} \Sigma \mathbf{V}^T, \, \mathbf{R} = \mathbf{U}\mathbf{V}^T

## Slide 117: Virtual Humans – Winter 24/25
Lecture 4_1 – ICP: Iterative Closest Points
Prof. Dr.-Ing. Gerard Pons-Moll
University of Tübingen / MPI-Informatics

## Slide 118: Non-rigid Articulated Registration
Notes: In reality we need to non-rigidly align bodies. Not only rotation, translation and scale, but also articulation and non-rigid alignment

## Slide 119: What is missing?
Given correspondences, we can find the optimal rigid alignment with Procrustes.
PROBLEMS:
How do we find the correspondences between shapes ?
How do we align shapes non-rigidly ?
Notes: We have two remaining problems. How do we find the correspondences. How do we align non-rigidly

## Slide 120: ICP and alignment based on optimisation
Optimising alignment and correspondences using Iterative Closest Point (ICP).
Alignment through continuous optimisation.

## Slide 121: How do we find correspondences?

## Slide 122: How do we find correspondences?

## Slide 123: How do we find correspondences?
Notes: Based on local features? This is often ambiguous! Local parts look the same

## Slide 124: How do we find correspondences?
compact notation: f contains translation, rotation and isotropic scale
?
Closest point to target shape point
The optimisation is over:
  the transform
  the correspondences
Notes: E(\mathcal{C},f) = \sum_i \min_{\mathbf{x}\in\mathbf{X}} \|f(\mathbf{x})-\mathbf{y}_i \|^2
\mathcal{C}=\{(\mathbf{x}_i,\mathbf{y}_i)\}_i^N

## Slide 125: How do we find correspondences?
The idea was to minimise the sum of distances between the one set of points and the other set, transformed
compact notation: f contains translation, rotation and isotropic scale
?

## Slide 126: Ideas
The idea was to minimise the sum of distances between the one set of points and the other set, transformed
What if we estimate the correspondences?
compact notation: f contains translation, rotation and isotropic scale

## Slide 127: Solution: Iteratively find correspondences
The idea was to minimise the sum of distances between the one set of points and the other set, transformed
What if we estimate the correspondences?
iteration
Given current best transformation,
which are the closest correspondences?
Given current best correspondences,
which is the best transformation?
original unsorted points
compact notation: f contains translation, rotation and isotropic scale

## Slide 128: Alternate between finding correspondences and finding the optimal transformation
The idea was to minimise the sum of distances between the one set of points and the other set, transformed
What if we estimate the correspondences?
Given current best transformation,
which are the closest correspondences?
Given current best correspondences,
which is the best transformation?
compact notation: f contains translation, rotation and isotropic scale
iteration
original unsorted points
Notes: To what machine learning method does this remind you of? —> Expectation maximisation. In K-means and fitting mixture of Gaussians there is a similar type of alternation.

## Slide 129: Make up reasonable correspondences
Notes: \xwo_i = \arg\min_{\xwo}\|\Tt\xwo -\y \|^2
%\y
%\xwo_0
%\xwo_1

## Slide 130: Make up reasonable correspondences
Neutral initialization.
Initializing t to align centroids should work better!
Notes: \xwo_i = \arg\min_{\xwo}\|\Tt\xwo -\y \|^2
%\y
%\xwo_0
%\xwo_1

## Slide 131: Make up reasonable correspondences

## Slide 132: Solve for the best transformation
solve with procrustes

## Slide 133: Apply it …

## Slide 134: and iterate!

## Slide 135: and iterate!

## Slide 136: and iterate!

## Slide 137: and iterate!

## Slide 138: and iterate!

## Slide 139: Iterative Closest Point (ICP)
Initialize

## Slide 140: Iterative Closest Point (ICP)
Initialize
Compute correspondences according to current best transform

## Slide 141: Iterative Closest Point (ICP)
Initialize
Compute correspondences according to current best transform
Compute optimal transformation ( )with Procrustes

## Slide 142: Iterative Closest Point (ICP)
Initialize
Compute correspondences according to current best transform
Compute optimal transformation ( )with Procrustes
Terminate if converged (error below a threshold), otherwise iterate

## Slide 143: Iterative Closest Point (ICP)
Initialize
Compute correspondences according to current best transform
Compute optimal transformation ( )with Procrustes
Terminate if converged (error below a threshold), otherwise iterate
Converges to local minima

## Slide 144: Is ICP the best we can do?
Iteration j:
compute closest points
compute optimal transformation with Procrustes
apply transformation
terminate if converged, otherwise iterate

## Slide 145: Closest points
Brute force is O(n2)
For every source point find a neighbor point on the source shape

## Slide 146: Closest points
Tree based methods (e.g. kdtree) have avg. complexity log(n)
Random point sampling also reduces the running time

## Slide 147: ICP: Tips to avoid local minima
Always find correspondences from target to source! Proper data term
Outliers —> Robust cost functions
Use additional information (e.g. normals)
Compute transformation based on greedy subsets of points: RANSAC

## Slide 148: A much better objective: Point-to-surface distance
Notes: This results in a point-to-surface distance. If we zoom in a triangle with vertices v_0 to v_2
\mathbf{y}_0 \in \mathbf{Y}

## Slide 149: Closest points: avoid local minima
Point-to-point distance
Notes: and a query point s from the surface of the scan, a point-to-surface distance would find the closest vertex on the registration, in this case x1. This is not a good distance estimation, since

## Slide 150: Closest points: avoid local minima
Point-to-surface distance
Notes: the closest distance to the surface is the one to a point within the triangle. Although this seems rather obvious, it is rather common to find papers using the point to surface distance. The formulation of the derivatives of point-to-surface distance is more complicated, but results are substantially better.

## Slide 151: Is ICP the best we can do?
Iteration j:
compute closest points
compute optimal transformation with Procrustes
apply transformation
terminate if converged, otherwise iterate

## Slide 152: Best transformation?
Procrustes gives us the optimal rigid transformation and scale given correspondences
What if the deformation model is not rigid ?
Can we generalise ICP to non-rigid deformation ?

## Slide 153: Iterative Closest Point (ICP)
Iteration j:
compute closest points  Which direction to move?
compute optimal transformation with Procrustes
apply transformation
terminate if converged, otherwise iterate

## Slide 154: Iterative Closest Point (ICP)
Iteration j:
compute closest points  Which direction to move?
compute optimal transformation with Procrustes 
apply transformation
terminate if converged, otherwise iterate
Compute a transform that reduces the error
Notes: The first step gives us correspondences. The direction I should move towards. In the second step we have to compute the optimal transformation.

## Slide 155: Gradient-based ICP
Iteration j:
compute closest points  Which direction to move?
compute optimal transformation with Procrustes 
apply transformation
terminate if converged, otherwise iterate
Compute descent step by linearising the energy
Jacobian of distance-based energy
Notes: If we have a more complicated paramterization of shape deformation, we can linearlize the energy with respect to transformation f parameters

## Slide 156: Gradient-based ICP
If f is a rigid transformation we can solve this minimisation using Procrustes
If f is a general non-linear function ?
Gradient descent:
For least squares, is there a better optimisation method ? yes: Gauss-Newton based methods.
Notes: Note the derivative is not with respect to the function. In practice the function is parameterised, and the derivative is with respect to those parameters.
\arg\min_f E(f) = \arg\min_f \sum_i\|f(\mathbf{x}_i^{j+1})-\mathbf{y}_i\|^2
f^{k+1} = f^k + \nabla_f E(f)

## Slide 157: Gradient-based ICP
Energy:
Consider the correspondences fixed in each iteration j+1
Compute gradient of the energy around current estimation
Apply step (gradient descent, dogleg, LM, BFGS…)
terminate if converged, otherwise iterate (go to step 2)
(for example )

## Slide 158: Gradient-based ICP

## Slide 159: Why is convergence on the left less smooth?
Point to point objective
Point to surface objective

## Slide 160: Gradient-based ICP
Energy:
Consider the correspondences fixed in each iteration j+1
Compute gradient of the energy around current estimation
Apply step (gradient descent, dogleg, LM, BFGS…)
terminate if converged, otherwise iterate

## Slide 161: Gradient-based ICP
Gradient: derivative of the sum of squared distances with respect to transformation f parameters
Notes: \documentclass[10pt]{article}
\usepackage[usenames]{color} %used for font color
\usepackage{amssymb} %maths
\usepackage{amsmath} %maths
\usepackage[utf8]{inputenc} %useful to type directly diacritic characters
\newcommand*{\tran}{^{\mkern-1.5mu\mathsf{T}}}
\newcommand{\Ss}{\mathbf{S}}
\newcommand{\X}{\mathbf{X}}
\newcommand{\Tt}{\mathbf{T}}
\newcommand{\mX}{\bar{\mathbf{X}}}
\newcommand{\x}{\mathbf{x}_i}
\newcommand{\xwoi}{\mathbf{x}}
\newcommand{\ywoi}{\mathbf{y}}
\newcommand{\hx}{\hat{\mathbf{x}}_i}
\newcommand{\xwo}{\mathbf{x}}
\newcommand{\hxwo}{\hat{\mathbf{x}}}
\newcommand{\mx}{\bar{\mathbf{x}}}
\newcommand{\mxi}{\bar{\mathbf{x}_i}}
\newcommand{\Pb}{\mathbf{P}}
\newcommand{\mPb}{\bar{\mathbf{P}}}
\newcommand{\pb}{\mathbf{p}_i}
\newcommand{\mpb}{\bar{\mathbf{p}}}
\newcommand{\mpbi}{\bar{\mathbf{p}_i}}
\newcommand{\Y}{\mathbf{Y}}
\newcommand{\mY}{\bar{\mathbf{Y}}}
\newcommand{\y}{\mathbf{y}_i}
\newcommand{\my}{\bar{\mathbf{y}}}
\newcommand{\myi}{\bar{\mathbf{y}_i}}
\newcommand{\U}{\mathbf{U}}
\newcommand{\V}{\mathbf{V}}
\newcommand{\R}{\mathbf{R}}
\newcommand{\A}{\mathbf{A}}
\newcommand{\trans}{\mathbf{t}}
%E &\equiv \sum_i \| s \R \x + \trans - \y \|^2 \equiv \sum_i \| f(\x) - \y \|^2\\
%E &\equiv \sum_i \min_\xwoi\|f(\xwoi) - \y \|^2%E &\equiv \sum_i \| s \R \x + \trans - \y \|^2 \equiv \sum_i \| \Tt \mxi - \myi \|^2\\
%\hx &= \arg\min_\xwoi \| f(\xwoi) - \y\|^2 \\
%f &= \arg\min_f \sum_i \| f(\hx) - \y \|^2\\
%f^0 &= \{\R=\mathbf{I}, \trans=\mathbf{0}, s=1\} \\
%f^0 &= \{\R=\mathbf{I}, \trans=\frac{\sum{\y}}{N} - \frac{\sum{\x}}{N}, s=1\} \\
%\xwoi_i^1 &= \arg\min_{\xwoi \in \X} \| f^0(\xwoi) - \y\|^2 \\
%f^{j} &= \arg\min_f \sum_i \| f(\x) - \y \|^2\\
%\x^{j+1} &= \arg\min_{\xwoi \in \X} \| f^j(\xwoi) - \y\|^2 \\
%f^{j+1} &= \arg\min_f \sum_i \| f(\x^{j+1}) - \y \|^2\\
%E^{j+1} &= \sum_i \| f^j(\x) - \y \|^2\\
%^\xwoi_0
%\xwoi_i^{j+1} &= \arg\min_{\xwoi \in \X} \| f^j(\xwoi) - \y\|^2 \\
%\X \equiv f^0(\X)
%E &\equiv \sum_i \| \min_\xwoi f(\xwoi) - \y \|^2\\
%J^{j+1} &= \frac{\delta E}{\delta f}(f^j)
%f^{j+1} = k_{\mathrm{step}}(J^{0\ldots j+1}, f^{0\ldots j})
f^{j+1} = f^{j} - \alpha J^{j+1}

## Slide 162: Gradient-based ICP
Gradient: derivative of the sum of squared distances with respect to transformation f parameters
Each derivative is easy
  Who wants to writes it down?
Notes: \documentclass[10pt]{article}
\usepackage[usenames]{color} %used for font color
\usepackage{amssymb} %maths
\usepackage{amsmath} %maths
\usepackage[utf8]{inputenc} %useful to type directly diacritic characters
\newcommand*{\tran}{^{\mkern-1.5mu\mathsf{T}}}
\newcommand{\Ss}{\mathbf{S}}
\newcommand{\X}{\mathbf{X}}
\newcommand{\Tt}{\mathbf{T}}
\newcommand{\mX}{\bar{\mathbf{X}}}
\newcommand{\x}{\mathbf{x}_i}
\newcommand{\xwoi}{\mathbf{x}}
\newcommand{\ywoi}{\mathbf{y}}
\newcommand{\hx}{\hat{\mathbf{x}}_i}
\newcommand{\xwo}{\mathbf{x}}
\newcommand{\hxwo}{\hat{\mathbf{x}}}
\newcommand{\mx}{\bar{\mathbf{x}}}
\newcommand{\mxi}{\bar{\mathbf{x}_i}}
\newcommand{\Pb}{\mathbf{P}}
\newcommand{\mPb}{\bar{\mathbf{P}}}
\newcommand{\pb}{\mathbf{p}_i}
\newcommand{\mpb}{\bar{\mathbf{p}}}
\newcommand{\mpbi}{\bar{\mathbf{p}_i}}
\newcommand{\Y}{\mathbf{Y}}
\newcommand{\mY}{\bar{\mathbf{Y}}}
\newcommand{\y}{\mathbf{y}_i}
\newcommand{\my}{\bar{\mathbf{y}}}
\newcommand{\myi}{\bar{\mathbf{y}_i}}
\newcommand{\U}{\mathbf{U}}
\newcommand{\V}{\mathbf{V}}
\newcommand{\R}{\mathbf{R}}
\newcommand{\A}{\mathbf{A}}
\newcommand{\trans}{\mathbf{t}}
%E &\equiv \sum_i \| s \R \x + \trans - \y \|^2 \equiv \sum_i \| f(\x) - \y \|^2\\
%E &\equiv \sum_i \min_\xwoi\|f(\xwoi) - \y \|^2%E &\equiv \sum_i \| s \R \x + \trans - \y \|^2 \equiv \sum_i \| \Tt \mxi - \myi \|^2\\
%\hx &= \arg\min_\xwoi \| f(\xwoi) - \y\|^2 \\
%f &= \arg\min_f \sum_i \| f(\hx) - \y \|^2\\
%f^0 &= \{\R=\mathbf{I}, \trans=\mathbf{0}, s=1\} \\
%f^0 &= \{\R=\mathbf{I}, \trans=\frac{\sum{\y}}{N} - \frac{\sum{\x}}{N}, s=1\} \\
%\xwoi_i^1 &= \arg\min_{\xwoi \in \X} \| f^0(\xwoi) - \y\|^2 \\
%f^{j} &= \arg\min_f \sum_i \| f(\x) - \y \|^2\\
%\x^{j+1} &= \arg\min_{\xwoi \in \X} \| f^j(\xwoi) - \y\|^2 \\
%f^{j+1} &= \arg\min_f \sum_i \| f(\x^{j+1}) - \y \|^2\\
%E^{j+1} &= \sum_i \| f^j(\x) - \y \|^2\\
%^\xwoi_0
%\xwoi_i^{j+1} &= \arg\min_{\xwoi \in \X} \| f^j(\xwoi) - \y\|^2 \\
%\X \equiv f^0(\X)
%E &\equiv \sum_i \| \min_\xwoi f(\xwoi) - \y \|^2\\
%J^{j+1} &= \frac{\delta E}{\delta f}(f^j)
%f^{j+1} = k_{\mathrm{step}}(J^{0\ldots j+1}, f^{0\ldots j})
f^{j+1} = f^{j} - \alpha J^{j+1}

## Slide 163: Gradient-based ICP
Gradient: derivative of the sum of squared distances with respect to transformation f parameters
Each derivative is easy
  Who wants to writes it down?
Chain rule and automatic differentiation!
Notes: \documentclass[10pt]{article}
\usepackage[usenames]{color} %used for font color
\usepackage{amssymb} %maths
\usepackage{amsmath} %maths
\usepackage[utf8]{inputenc} %useful to type directly diacritic characters
\newcommand*{\tran}{^{\mkern-1.5mu\mathsf{T}}}
\newcommand{\Ss}{\mathbf{S}}
\newcommand{\X}{\mathbf{X}}
\newcommand{\Tt}{\mathbf{T}}
\newcommand{\mX}{\bar{\mathbf{X}}}
\newcommand{\x}{\mathbf{x}_i}
\newcommand{\xwoi}{\mathbf{x}}
\newcommand{\ywoi}{\mathbf{y}}
\newcommand{\hx}{\hat{\mathbf{x}}_i}
\newcommand{\xwo}{\mathbf{x}}
\newcommand{\hxwo}{\hat{\mathbf{x}}}
\newcommand{\mx}{\bar{\mathbf{x}}}
\newcommand{\mxi}{\bar{\mathbf{x}_i}}
\newcommand{\Pb}{\mathbf{P}}
\newcommand{\mPb}{\bar{\mathbf{P}}}
\newcommand{\pb}{\mathbf{p}_i}
\newcommand{\mpb}{\bar{\mathbf{p}}}
\newcommand{\mpbi}{\bar{\mathbf{p}_i}}
\newcommand{\Y}{\mathbf{Y}}
\newcommand{\mY}{\bar{\mathbf{Y}}}
\newcommand{\y}{\mathbf{y}_i}
\newcommand{\my}{\bar{\mathbf{y}}}
\newcommand{\myi}{\bar{\mathbf{y}_i}}
\newcommand{\U}{\mathbf{U}}
\newcommand{\V}{\mathbf{V}}
\newcommand{\R}{\mathbf{R}}
\newcommand{\A}{\mathbf{A}}
\newcommand{\trans}{\mathbf{t}}
%E &\equiv \sum_i \| s \R \x + \trans - \y \|^2 \equiv \sum_i \| f(\x) - \y \|^2\\
%E &\equiv \sum_i \min_\xwoi\|f(\xwoi) - \y \|^2%E &\equiv \sum_i \| s \R \x + \trans - \y \|^2 \equiv \sum_i \| \Tt \mxi - \myi \|^2\\
%\hx &= \arg\min_\xwoi \| f(\xwoi) - \y\|^2 \\
%f &= \arg\min_f \sum_i \| f(\hx) - \y \|^2\\
%f^0 &= \{\R=\mathbf{I}, \trans=\mathbf{0}, s=1\} \\
%f^0 &= \{\R=\mathbf{I}, \trans=\frac{\sum{\y}}{N} - \frac{\sum{\x}}{N}, s=1\} \\
%\xwoi_i^1 &= \arg\min_{\xwoi \in \X} \| f^0(\xwoi) - \y\|^2 \\
%f^{j} &= \arg\min_f \sum_i \| f(\x) - \y \|^2\\
%\x^{j+1} &= \arg\min_{\xwoi \in \X} \| f^j(\xwoi) - \y\|^2 \\
%f^{j+1} &= \arg\min_f \sum_i \| f(\x^{j+1}) - \y \|^2\\
%E^{j+1} &= \sum_i \| f^j(\x) - \y \|^2\\
%^\xwoi_0
%\xwoi_i^{j+1} &= \arg\min_{\xwoi \in \X} \| f^j(\xwoi) - \y\|^2 \\
%\X \equiv f^0(\X)
%E &\equiv \sum_i \| \min_\xwoi f(\xwoi) - \y \|^2\\
%J^{j+1} &= \frac{\delta E}{\delta f}(f^j)
%f^{j+1} = k_{\mathrm{step}}(J^{0\ldots j+1}, f^{0\ldots j})
f^{j+1} = f^{j} - \alpha J^{j+1}

## Slide 164: Automatic differentiation
write as if it was numpy code
results in expression tree with jacobians available at each step

## Slide 165: Gradient-based ICP
Energy:
Consider the correspondences fixed in each iteration j+1
Compute gradient of the energy around current estimation
Apply step (gradient descent, dogleg, LM, BFGS…)
terminate if converged, otherwise iterate

## Slide 166: Why Gradient-based ICP?
Formulation is much more generic: the energy can incorporate other terms, more parameters, etc
A lot of available software for solving this least squares problem (cvx, ceres, …)
However, the resulting energy is non-convex for general deformation models. Optimisation can get trapped in local minima.

## Slide 167: Take-home message
Procrustes is optimal for rigid alignment problems with known correspondences. For other problems:
We can compute correspondences and solve for the best transformation iteratively with Iterative Closest Point (ICP)

## Slide 168: Slide credits
Javier Romero